## Slide 1: MERIF WORKSHOP ORBIT/COSMOS Introduction (Open Access Research Testbed for Next-Generation Wireless Networks)/(Cloud Enhanced Open Software Defined Mobile Wireless Testbed for City-Scale Deployment)
Michael Sherman, Rutgers University
Slides from Ivan Seskar

## Slide 2: Orbit Project Rationale (2003)
Wireless testbeds motivated by:
  cost & time needed to develop experimental prototypes
  need for reproducible protocol evaluations
  large-scale system studies (...emergent behavior)
  growing importance of cross-layer protocol studies
  creation of communities for wireless network research
ORBIT: open-access multi-user facility for experimental wireless networking research primarily in unlicensed bands
  ~24/7 service facility with remote access
  open interfaces for flexible layer 2,3 & cross-layer protocols
  extensive measurements at PHY, MAC and Net layers
  support for wide range of radio system scenarios

## Slide 3: ORBIT
Proposal: Build radio grid emulator (phase I) and field trial network (phase II)
Emulator used for detailed protocol evaluations in reproducible complex radio environments
Field trial network for further real-world evaluation & application trials

## Slide 4: Orbit Hardware
80 ft ( 20 nodes )
70 ft ( 20 nodes )
Control switch
Data
switch
Application Servers
(User applications/ Delay nodes/ Mobility Controllers / Mobile Nodes)
Internet VPN Gateway / Firewall
Back-end servers
Front-end
Servers
Gigabit backbone
VPN Gateway to
Wide-Area Testbed
SA1
SA2
SAP
IS1
IS2
ISQ
RF/Spectrum Measurements
Interference Sources

## Slide 5: ORBIT Radio Node (2004/2005)
CPU
VIA
C3 1Ghz
512 MB
RAM
CPU
Rabbit Semi
RCM3700
Gigabit
Ethernet
(control)
Gigabit
Ethernet
(data)
Intel/Atheros
miniPCI
802.11
a/b/g
10 BaseT
Ethernet
(CM)
PCI
22.1Mhz
1 Ghz
pwr/reset
volt/temp
20 GB
DISK
Serial
Console
Power
Supply
110
VAC
RJ11 NodeIdBox
+5v standby
Version 0: COTS:
  Proof of concept
  Prototyping platform
Version 1: Custom design:
  Functional requirements
  Manageability
  Power consumption
  Cost
Version 2: Custom design with other attached devices:
  Bluetooth
  ZigBee
  GNU Radio
Intel/Atheros
miniPCI
802.11
a/b/g

## Slide 6: ORBIT Radio Node Gen 2 Photo Album
ORBIT Radio Node
with integrated Chassis Manager
Non-Grid Node
Chassis Manager

## Slide 7: Version 2.5: Back to COTS (2007)
The COTS 2nd generation node:
  Off the shelf motherboard
  Custom indoor or outdoor (weatherproof) enclosure
  Control manager (CM) with optional GPS and GPRS

## Slide 8: ORBIT Radio Node Versions
Core 2 Quad with Q35 Express chipset
4 GB DDR2
2 x Gigabit Ethernet ports
PCI-Express X16
Mini-PCI socket
8 x USB 2.0
2 x COM
Core 2 Duo with GM45 chipset
8 GB DDR3
2 x Gigabit Ethernet ports
PCI-Express X16
PCI Express mini socket
Mini-PCI socket
8 x USB 2.0
2 x COM
I7-4770 3.4 GHz Q87T Express chipset
16 GB DDR3
2 x Gigabit Ethernet ports
PCI-Express 2.0 X16
2 x Mini-PCIexpress socket
8 x USB 3.0
OOB Mgmgt.
Xeon E5-2600v3 with 18 cores
64 GB DDR4
2 x 10G Ethernet ports
2 x Gigabit Ethernet ports
PCI-Express 3.0 X16
8 x USB 3.0
OOB Mgmgt.
Version 3 (2010/2011)
Version 4 (2015/2016)

## Slide 9: Fixed Function Radio Devices: 802.11 (a,b,g,n,ac,ad), Zigbee, BT/BLE
Atheros Dual Band (5212)
Dual-diversity with 0-18 dBm (1 dBm steps)
PCI 2.3 and PC Card 7.1
Drivers: madwifi and ath5k
Intel Dual Band 2915ABG
Dual-diversity with -12-+20 dBm (1 dBm steps)
Drivers: ipw2200
Belkin F8T003 and F8T010
Bluetooth v1.1 compliant
Range of 10m (100m)
Driver: BlueZ
Netgear WNDA3100
Based on Atheros AR9170+AR9104
2x2 MIMO
6.5 - 300 Mbps
Driver: ath9k
D-LINK DWA-140
Based on Ralink RT2870
2x2 MIMO
20/40 MHz support
6.5 - 300 Mbps
Driver*: rt2x00
Atmega (4MHz), MSP430 (8MHz)
CC2420 250kbps 2.4GHz IEEE 802.15.4 (ZigBee) Chipcon Wireless Transceiver
Sensors - Temperature, Light, Humidity
Driver: Motes (Contiki)

## Slide 10: SDR Devices: USRP/USRP2/B210/X310
IF 0-100 MHz (50 MHz transmit)
  128 MS/s DAC
  64 MS/s ADC
USB bus (W = 8 MHz)
Channelizer code in Altera Cyclone FPGA
2 RF board slots
IF -200 MHz (80 MHz receive)
  100 MS/s 14-bit dual (IQ) ADCs 400 MS/s 16-bit dual (IQ) DACs
Gigabit Ethernet (W = 25 MHz)
FPGA w/Multipliers (Xilinx Spartan 3), 1 MB SRAM
1 RF board slot
Xilinx Spartan-6 FPGA
Dual channel AD9361 RFIC transceiver (70 MHz – 6 GHz with 56 MHz baseband)
USB 3.0 connectivity
Xilinx Kintex-7 FPGA (XC7K410T)
2 x 10 Gigabit Ethernet
1 x SBX RF Daughterboard (400-4400 MHz Rx/Tx with 120 MHz baseband)
1 x CBX RF Daughterboard (1200-6000 MHz Rx/Tx with 120 MHz baseband)

## Slide 11: Latest ORBIT Nodes
8 USRP X310s:
  Dual 160 MHz baseband
  2 x 10G optical Ethernet interconnects
  Large Kintex FPGA with:
Resource Type | Number
DSP48 Blocks | 58K
Block Rams (18 kB) | 14K
Logic Cells | 7.2M
Slices (LUTs) | 1.5M
Movable mini-racks in four corners
Core Computing with SDN
Rack with 32 machines:
  2 x 12 core CPU
  2 x 25G optical Ethernet interconnects
  100G TOR SDN switch

## Slide 12: ORBIT SDN Deployment

## Slide 13: ORBIT Grid

## Slide 14: Sandboxes
To support development and reduce pressure on the grid
  Console and a pair of nodes and devices focused on particular technology
Except for two specialized sandboxes:
SB4
SB9
Software Defined Networking
Tight topology control

## Slide 15: ORBIT Outdoor Infrastructure (WiMAX/LTE)
Outdoor Unit (ODU)
RF Module
( sector)
Base
Module
Omni-directional antenna
(elev. < 6ft above roof!)
Experimental readings at one location
CINR = 29 RSSI = -51
Rt. 1 Campus WiMAX Coverage
ORBIT
Vehicular
Node
WiMAX: Intel 5150/5350/6250 LTE: Netgear AC341U
Android based portable platform
HTC EVO 4G
Nexus 5
Galaxy 6
Notes: 15

## Slide 16: GENI Wireless Deployment
Wayne State
Clemson
U Michigan
Columbia
UMass
U Wisconsin
Madison
U Colorado
Boulder
UCLA
Stanford
Rutgers
Temple
Drexel
NYU
32 LTE and WiMAX BS on 14 campuses
SDN (Click and OVS based) datapath/backbone
Sliced, virtualized and interconnected (100 Gbps) through Internet2
10 mini-ORBIT deployments some with SDRs
Kettering
Utah

## Slide 17: COSMOS Project Vision
Latency and compute power are the two new dimensions for characterizing wireless access
Latency for 4G cellular > 50 ms, while targets for 5G are <10 ms
Edge computing is an enabler for real-time services
COSMOS will enable researchers to investigate ultra-high speed (~Gbps), low latency (<5ms), and edge computing (~10-100 GIPS)
COSMOS = Cloud Enhanced Open Software Defined Mobile Wireless Testbed for City-Scale Deployment

## Slide 18: System Architecture
COSMOS architecture has been developed to realize ultra-high BW, low latency and tightly coupled edge computing
Key design challenge: Gbps performance + full programmability at the radio level
Developed a fully programmable multi-layered (i.e. radio, network and cloud) system architecture for flexible experimentation

## Slide 19: System Architecture (cont’d)
System design based on three levels of SDR radio node (S,M,L) with M,L connected via fiber to optical WDM transport
SDN-based backhaul and compute services, with access to ORBIT, GENI…
COSMOS control center and general purpose cloud at Rutgers via 32 AoA PoP

## Slide 20: Planned Deployment
West Harlem
Area: ~1 sq. mile
~9 Large Sites ~40 Medium sites
Fiber optic connection from most sites
~200 Small nodes
  Including vehicular and hand-held
Fiber connection to NYU Data Center, Rutgers, GENI/I2
Interaction with smart community & innovation initiatives (Gigabit center, etc.)

## Slide 21: Key Technologies - SDR
All-software solution adopted for radio technology
Advanced SDR Radio Nodes at various performance levels and form factors
Design goal: 400 Mhz – 6 Ghz + 28 Ghz and 60 Ghz bands, ~500 Mhz BW, Gbps
Signal processing can be spread between radio node & edge cloud RAN
COSMOS SDR Node, SDR Tray and RF Frontend Tray
Mobile SDR Node with: B210, B205
Ettus E312

## Slide 22: Sub-6GHz SDR Devices
USRP-2974 (Main Experimentation SDR) | 
System on module | Congatec COM Express conga-TS170 (Quad Core i7 6822EQ @ 2 GHz)
RAM | 8GB DDR4
Ethernet | 2 x 10 Gbps
ADC/DAC | 2 x 200 MHz @ 14 bit/200 MHz @ 16 bit
RF | 2 x 10 MHz to 6 GHz / 160 MHz BW
FPGA | Kintex-7 XC7K410T with 1GB RAM
USRP-N310 (Main Monitoring SDR) | 
System on Chip | Zynq-7100 (Dual-core ARM Cortex-A9 @ 800 MHz)
RAM | 1 GB DDR3
Ethernet | 2 x 10 Gbps
ADC/DAC | 4 x {122.88, 125, 153.6 MS/s} @ 16 bit/@ 14 bit
RF | 4 x 10 MHz to 6 GHz / 100 MHz BW
FPGA | Zynq-7100 SoC with 1GB RAM

## Slide 23
mmWave a key new technology for the testbed, with limited availability of components
Leveraging ongoing CU collaboration with IBM to provide mmWave phased arrays (64 antennas, 8 beams) for 28 Ghz
Extensive mmWave systems expertise at NYU, including prototype systems and channel measurements
mmWave components from IBM
NYU Channel Measurements
Key Technologies – mmWave

## Slide 24
Package dimensions: 70mm x 70mm x 2.7mm
Flip-chip assembly for 4 ICs
655 BGA w/ 1.27mm pitch supporting multiple power domains, IF (TX & RX) and LO signals, Digital control and ref clock signals
4-chip (130nm SiGe, 166 mm2) antenna module with two operation modes: 2 x 64 element beams or 8 x 16-element beams
Performance Summary | 
Elements per chip | 32 TX/RX
Elements in package | 128 TX/RX
Phase resolution (deg) | 5
RMS phase error (deg) | 0.8
TX Psat (dBm) per element | 16
TX Op1dB (dBm) per element | 13.5
TX EIRP per package per pol. @Psat (dBm) | 54
H-pol, ±50°
E-plane
H-plane
V-pol, ±50°
E-plane
H-plane
Key Technologies – mmWave (cont’d)

## Slide 25: mmWave Baseband Devices
Initially: USRP based BB (2 channels @ 100 MHz) with 2 x 10 Gbps
Full deployment: RFSoC based (up to 8 channels @ 400 MHz) with 100 Gbps
RF-ADC | 8 x 4.096 Gsps @ 12 bit
RF-DAC | 8 x 6.554 Gsps @ 14 bit
Logic Cells | 930,000
Memory (Mb) | 60.5 [Mb]
DSP Slices | 4,272
33G Transceivers | 16*

## Slide 26: Medium Node
Variants based on building blocks:
mmWave RF front-end
mmWave SDR BB
Sub-6GHz RF front-end
Sub-6GHz SDR BB
Sub 6GHz monintoring RF front-end
RF-over-fiber
10/100G (Ethernet+Optical)
Standard compute platform (PC)
WiFI devices

## Slide 27: Key Technologies – Optical Net
Fast and low latency optical x-haul network using 3D MEMS switch and WDM ROADM
  Configure wide range of topologies
  Experiment on converged fiber/wireless networks
Enables fast front-haul/mid-haul/back-haul connectivity between radio nodes and edge cloud
SDN control plane for both optical and Ethernet switching
Leverages results from CIAN NSF ERC, EAGER dark fiber project at Columbia
MEMS Switch
ROADM (whitebox)

## Slide 28: CALIENT & Lumentum
Calient MEMS Space switch
  320x320 any to any optical circuit switch
  ~2db loss, ~25ms switching time
  Openflow, netconf, etc.
Lumentum Whitebox20
  20 port degree 1 ROADM
  C band DWDM
  Supports netconf

## Slide 29
Optical Deployment View

## Slide 30: Key Technologies – SDN & Cloud
SDN control plane used to control x-haul and cloud server connectivity
Open Network Operating System (ONOS) with radio API extensions
Compute clusters collocated with radio nodes (M,L) with choice of CPU, GPU and FPGA accelerators
Also, users have access to regular cloud racks for L3 applications (GENI & CloudLab clusters at WINLAB)
SDN Switching Rack

## Slide 31: DELL Switches
Data Plane switching:
  Dell Z9100-ON Switches
  Commodity 100g ethernet switching
  Broadcom Tomahawk Chipset
  Openflow 1.3
  Supports alternate operating systems via ONIE
Control Plane switching:
  Dell S4048-ON
  Cost effective 10g switching
  Used for physically separate control plane

## Slide 32: Compute Nodes
Dell R740XD
  Dual 12 Core CPU
  192GB Ram
  Dual 25G NIC w RDMA
  Nvidia V100 GPU
  Xilinx Alveo U200 FPGA,
    2x 100g port

## Slide 33
Cloud Architecture

## Slide 34
Layer-2 Deployment View

## Slide 35: COSMOS Summary
Focus on ultra high bandwidth, low latency, edge cloud
Open platform (building on ORBIT) integrating mmWave, SDR, and optical x-haul
1 sq mile densely populated area in West Harlem
Local community outreach
Research community:
  Develop future experiments, provide input
  (short term) get involved in the educational outreach
More information: https://advancedwireless.org/ https://www.orbit-lab.org https://www.cosmos-lab.org